Taiwan Power Company
Announcement
Date: 2025/11/21
Invitation to Bid No. TPC11501-A6

Taiwan Power Company intends to procure the following commodity through open tender. The firms including foreign coal mine owners, foreign coal producers, foreign and local coal agents and trading companies, if interested in this tender, may obtain from this company the bidding documents and submit their bids to this company on or before the time as specified hereunder.

A. Description of Commodity:
400000 metric tons of bituminous coal for Taipower thermal power plant
B. Procurement Area:
The coal to be purchased by Taipower and delivered by a Bidder shall be
supplied from Australia, Canada, Mainland China, Kazakhstan, and the United States.
C. Period of obtaining Bidding Documents
Office hours from 2025/11/21 to 2025/12/1 (Taipei time)
D. Deadline for receiving Bids
05:00 p.m. 2025/12/1 (Taipei Time)
E. Time for opening Technical & Commercial Proposal
09:30 a.m. 2025/12/2 (Taipei Time)

Note:
1. The above 400000 metric tons of bituminous coal shall be shipped by Five (5) Panamax Size vessels.
2. Panamax Size vessel: 80000 metric tons plus/minus 10%.
3. Offeror may offer one or more than one shipment.
4. Bid bond: USD80000 or TWD2640000 per shipment.
5. Delivery period：February 2026 through April 2026.
6. The minimum acceptable quality specifications (based on ISO standards) shall be as follows:
Item	Maximum/Minimum
Gross Calorific Value (Kcal/Kg, as received)	5,900 Min*1
Total Moisture (%, as received)	15 Max*2
Ash Content (%, air dried)	15 Max
Total Sulfur Content (%, air dried)	0.7 Max
Volatile Matter (%, air dried)	26 Min
Fixed Carbon (%, air dried)	60 Max
Grindability (Hardgrove Index Value)	45 Min
Ash Fusion Temperature / (degree(s) Celsius, under reducing condition, H=W)	1,300 Min
Mercury Content (mg/Kg, dry basis)	0.12 Max
Size	50 x 0 mm
Size above 50 mm (%)	5 Max
Fines under 2 mm (%)	35 Max
Na2O in Ash (%)	Remark 3

Note:
1. Gross Calorific Value greater than 6,900 kcal/kg will be treated as 6,900 kcal/kg.
2. Total Moisture can be raised to 18% max, if Ash Content is less than 10%.
3. Na2O in Ash
(1) If the actual Ash Content (air dried) is greater than 7%,
Na2O in Ash is 2% Max; if both actual (a) CaO+MgO > Fe2O3, and actual (b) CaO+MgO+Fe2O3 > 20% are met, then Na2O in Ash can be raised to 5.0% Max.
(2) If the actual Ash Content (air dried) is equal to or less than 7%
Na2O in Ash is 3% Max; if actual CaO+MgO+Fe2O3 > 20% is met, then Na2O in Ash can be raised to 6.0% Max.
7. Bidding documents can be:
a. obtained at Taipower’s web-site address:
https://hc1.taipower.com.tw/2764/2865/2888/50831/50835/
b. provided by Taipower, at the request of interested entity by fax or E-mail, to the E-mail address as advised
c. obtained at R.O.C. e-Procurement System web-site address:
http://web.pcc.gov.tw/

If you have any question, please contact the following:
Address: 9F., No. 242 Roosevelt Road, Section 3, Zhongzheng Dist., Taipei City 100208, Taiwan, R.O.C.
Telephone: 886-2-23666752/886-2-23667399
Facsimile: 886-2-23670597
E-mail address: d0090404@taipower.com.tw
Attention: Department of Fuels, Taiwan Power Company